## Slide 1: VLAN & VTP
Course Code: COE 3206
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | Lab 11 | Week No: | 11 | Semester: | Fall 24-25
Lecturer: | Dr. Md Mehedi Hasan; mmhasan@aiub.edu |  |  |  | 
Course Title: Computer Networks

## Slide 2: Lecture Outline
Configuring VLANs
VTP Configuration

## Slide 3: Configuring VLANs
Introduction
Each VLAN must have a LAN number  Valid numbers are 1 to 4094
Normal VLANS 1 to 1005
  Stored in in vlan.dat file of Flash memory
  Normally used
Extended VLANS 1006 to 4094
  Stored in running configuration file
  Limited options
Factory set VLANs (cannot be changed)
  VLAN 1 ---Administrative VLAN or default VLAN (for Cisco switch)
  VLAN 1001 to 1005 used for Token ring and FDDI networks (Not used usually)
VLAN name is optional [1]
A technique of logically grouping of computers of LAN to limit broadcast
domain and improve security.

## Slide 4: Configuring VLANs….
Creation of VLANs
All configuration must be done in Global Configuration mode
VLAN Creation
# enable to access privileged exec mode.
# configure terminal to access global configuration mode.
# vlan 2 to create VLAN 2 and access VLAN configuration mode.
# name Production to name this VLAN Production.
# vlan 3 to create VLAN 3.
# name HR to name this VLAN HR [1].
Verify VLAN creation
show vlan brief

## Slide 5: Configuring VLANs….
Cisco IOS commands for creating four VLANs

## Slide 6: Configuring VLANs….
Modes of Interfaces
Access
  Used to connect an end device such as PC
Trunk
  Used to connect a connecting device such as another switch or a router to
  carry data for multiple VLANs
Access
Trunk if it is configured to carry
data of multiple VLANs

## Slide 7: Configuring VLANs….
Topic sub heading..
# enable to access privileged exec mode.
# configure terminal to access global configuration mode.
# interface fa0/1 to access FastEthernet port 0/1.
# switchport mode access to set this port into a nontrunking access mode.
# switchport access vlan 2 to set this port to use VLAN 2.
# interface fa0/2 to access FastEthernet port 0/2.
# switchport mode access to set this port into a nontrunking access mode.
# switchport access vlan 3 to set this port to use VLAN 3
# interface fa0/3 to access FastEthernet port 0/3
# switchport mode trunk to set this port into a trunking mode
Adding interface to a VLAN

## Slide 8: Configuring VLANs….
Commands for adding interfaces to a VLAN

## Slide 9: Configuring VLANs….
Verify members of a VLAN
Fa0/3
is not
shown
as it is
a trunk

## Slide 10: Configuring VLANs….
Adding multiple interfaces to a VLAN at a time
Adding multiple interfaces to a VLAN at a time

## Slide 11: Configuring VLANs….
Switch# show vlan | Displays VLAN information
Switch# show vlan brief | Displays VLAN information in brief
Switch# show vlan id 2 | Displays information about VLAN 2 only
Switch# show vlan name HR | Displays information about VLAN HR only
Verifying VLAN Information

## Slide 12: VTP Configuration
VTP configuration commands
B
A
C
D
E
F
Suppose
SW1: Sever
SW2 & SW3: Client
Switch(config)# vtp mode server
Switch(config)# vtp domain aiub
Switch(config)# vtp password 123
Switch(config)# vtp mode client
Switch(config)# vtp domain aiub
Switch(config)# vtp password 123
SW1
SW2
Switch(config)# vtp mode client
Switch(config)# vtp domain aiub
Switch(config)# vtp password 123
SW3

## Slide 13: Topic Heading..
VTP configuration verification
Verifying VTP
Switch# show vtp status | Displays general information about VTP configuration
Switch# show vtp counters | Displays the VTP counters for the switch

## Slide 14: router on stick

## Slide 15
References
[1] D. Liu, Cisco CCNA/CCENT Exam 640-802, 640-822, 640-816 Preparation Kit, Syngress
Publishing, Inc., 2009, pp. 549-567.
[2] W. Odom, Official Cert Guide CCNA 200-301 Volume 1, Pearson Education, Inc.,
2020, USA, p. 181.

## Slide 16
Books
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.